Machine adopts aviation aluminum alloy die casting material made.

Hydraulic power drive.

Aviation cable connector .

quality teflon coated heat plate.

application for PE/PP/PVC/PPR/PVDF etc.

machine details:

fusion range:160,180,200,225,250,280,315mm

butting deviation:under 0.3mm

temperature deviation: under 3degree.

total section of cylinders 22.02cm*cm

heating plate max temperature 299 degree.

operation pressure range :0---45Mpa

required time for welding temperature within 20min.

power:  heating plate 2.8kw/220v,  planing tool:1.1kw/220v,hydraulic unit:0.75kw/220v

package :   basic frame: wooden case:1010*665*550

hydraulic unit:wooden case:730*645*680

total weight:  189kgs

with CFR cost, LCL to Singapore port.： 1695usd in total.