KV-168A/F-120型

气动罩杯定型机

Type KV-168A/F-120

Bra Cup Moulding Machine

安装使用说明书

INSTALLATION MANUAL

汕头市宏基机械设备有限公司

SHANTOU HONG JI MACHINE EQUIPMENT CO.,LTD

联系人：MS chen peiying    TEL:0086-1581783595  Email:hongji-ying@163.com

欢迎使用我厂的产品！为了您和产品的安全，请您在吊运、安装、使用、保养、维修本产品前，仔细阅读使用说明书。

我们诚挚欢迎您对我厂产品提出宝贵的改进意见。

在编辑本说明书过程中已经力求完整，但不保证说明书没有任何漏失。如说明书与实际产品有不符之处，以实际产品为准，本公司最终解释权！

Welcome to choose our products! For you and the product's safety, please kindly be reminded to read this manual carefully before you start to transport ,install, operate ,repair and maintain our products .

Your suggestions for further improving our products are sincerely welcome.

We have been trying our best compiling our product's manual.mistakes or missing might be existed . If there is any unmatchable items ,please refers to the products .We will be responsible to provide you with final explanation!

目     录

- 机台标示说明及技术参数

- Machine Mark Specification

and Technical Parameter.............................................................................................................1-2

- 使用条件与操作

B、Working Conditions ,Working Safety....................................................................................3-4

- 使用与操作

C、Use and Operation................................................................................................................5-6

- 常用配件名称及规格

D、Name and Specification of Common Parts...........................................................................7

- 常见故障机现象及可能的故障点

E、Common Breakdown and

Possible Breakdown Points........................................................................................................8

- 电气接线图及电器原理图

F、Electric Circuit Map and

Electrical Equipment Principle Map..........................................................................................9

- 机台标识说明及技术参数

- Machine mark specification and technical parameter

标台标识说明

Machine mark pecification and

KV-168A/F-120气动子弹头定型机

KV-168A/F-120 bra cup machine

- 工作条件和工作安全注意

- Working conditions, Working safety

工作条件（Working conditions）

- 本机台所处环境温度一般应在0-40℃。

- 本机台所处环境相对温度一般在30%-95%。

- 本机台不应在露天环境下使用！

1.Temperature around the tool machine should be kept between 0-40℃。

2. Relative humidity to keep the machine should be between 30%-95%.

3. The machine is not allowed to be operated under open working conditions.

工作安全注意（Working safety）

操作人员在掌握有关安全操作的必要知识后方可使用。由于本机台属高温加工性能，因此操作者必须遵守下列安全规则。

Operators are not allowed to operate the machine until mastering the related knowledge on safety operation.

Due the the nature that the machine is operated with high temperature, Operatorsshould follow the hereby safety rules.

  - 本厂机台电源规格：220V

如果接错会造成整机电器原件浇坏请千万注意。

  - 220V电源为单相三蕊线，请千万分清地线与零线。

  - 机台需妥善接地，才可通电工作，以保证人身安全。

  - 机台安装时，应保持机台平稳，以勉开机时产生震动。

  - 开机台30分钟后严禁用手触摸模台及模具，以勉烫伤主。

  - 严禁把手伸手模具周边以内。

  - 遵守有关安全生产规定。

- The power norm of our machine: 220V.

Please be reminded that if connected in a wrong way, it will lead to damage the electrical equipment

- The 220V power is for single-phase tri-core wire, please also distinguish ground wire from zero wire.

- The machine is allowed to work after connected with ground wire for human being’s safety.

- When installing the machine, it will be necessary to keep stable for prevent vibration.

- Hand touching mould table and mould is prohibited in 30 minutes after being operated to prevent being burned.

- Do not put your hands to the surrounding area of mould.

- Follow the regulations about safe production.

- 使用与操作

C. Use and Operation

- 使用前的准备

1.1 本机台应有独立的电源总开关。

开关的负载量应大于机台实际功率5—10A。

1.2 接上与机台所要求的电压电源，认清火线、零线及地线。

1.3 接好气管接头，检查是否有漏气现象。

1.4 对润滑加油位和二联体加适量机油。

1.5 通电前必须接上地线。

1.6 打开电源开关，根据操作面板标识指示置手动位升起模台。

1.7 模具安装时必须切断电源，以免发生安全事故。

1.8 通电后根据用料要求和操作面板标识指示设定上下模温度。

1 Prepare to Use

1.1 Independent power switch is required for this machine .The loading capacity of the switch should be 5—10A larger than machine's actual power.

1.2 Connecting the required power of electric pressure ,distinguish fire wire from zero wire and wire.

1.3 Connecting ground wire before being powered .

1.6 Turn on the power switch .Lifting the model table according to the mark indication of operation.

1.7 Power should be off  when installing model to prevent any accident.

1.8 Set up mould temperature upon powering in accrodance to the materia requirement and operation table.

- 操作注意事项

2.1 机台长时间运行应经常对润滑加油位加油。

2.2 应该常检查二联体油位。

2.3 经常检查二联体上虑水瓶是否有积水，如有应及时放掉。

2.4 为了您的方便起见，本厂机台都没哟标识清楚的操作面板，您可根据自己需求进行操作。

2.5 本厂机台上的红绿灯按钮开关的作用分别是模具上升和模具下降。

2 Operation Notice

2.1 Often feeding oil to lubricate oil point when machine running for a long time.

2.2 Often check the oil point of two-unit.

2.3 Often check if there is any unexpected water in the water filtering bottle on the two-unit.

2.4 Operation Panel is installed for you to operate machines against your requirement and convenience.

2.5 The red and green button are respectively indicating modeling up or down.

四、常用配件名称及规格

D、 Name and specification of common parts

KV-168A/F-120型

| 名 称 | 规 格 | 电 压 |
| --- | --- | --- |
| 加热管 | 16*300*500W*8 set | 220V |
| 电磁阀 | 4V-310C-08 | 220V |
| 温控表 | 48*48 Temp controller (japan fuji) | 220V |
| 控温 | 可控硅 | 220V |
| 时间表 | H5CN | 220V |

Type KV-168A/F-120

| Name | specification | Electrictiy pressure |
| --- | --- | --- |
| Calorific pipe | 16*300*500W*8 set | 220V |
| Magnetic valve | 4V-310C-08 | 220V |
| Temperature control table | 48*48 Temp controller (japan fuji) | 220V |
| Control temperature | SCR/silicon controlled/thyristor | 220V |
| Time table | H5CN | 220V |

技术参照

Technical Parameter

KV-168A/F-120罩杯定型机

KV-168A/F-120 BRA CUP MACHINE

| 电源/功率 Power Supply/Power Rate | 220V/8KW |
| --- | --- |
| 模台尺寸 Dimensions of Mould Platform | 50mm×300mm |
| 机台尺寸 Dimensions of Main Machine | 1700mm×700mm×2300mm |
| 适用模具 Applicable Moulds | 文胸棉杯模具和鞋材模具 Mould for foam cup and shoe material mould |
| 重量 Weight | 300kg |

- 常见故障现象及可能的故障点

E. Common Breakdown and Possible Breakdown Points

KV168A/F-120

| 常见故障现象 | 可能的故障点 |
| --- | --- |
| 无电源指示或电压指示 | 1 电源开关损坏。2电压表烧坏。 |
| 加温不均匀或不能加温 | 1温控仪表损坏 2可控硅损坏。3电热管损坏。 |
| 气缸不能升降或 升降缓慢 | 1气缸密封圈损坏。2电磁阀线圈烧坏。 3电磁阀阀芯被卡住。4 电磁阀阀芯按钮开关没打开。 |
| 温控仪表显示值与设定值有误差 | 1加热管损坏或烧坏 2探温针损坏 3 温控仪损坏 |
| 不能启动 | 1启动开关损坏 2 电源短路 |

Type KV168A/F-120

| Common Breakdown | Possible Breakdown Point |
| --- | --- |
| No indication on power or no indication on electric pressure | 1 Power switch is broken. 2 Electric meter was burned |
| Heating is not fairly well-distributed or unable to heat | 1Temperature Control Table was broken 2Controll able silicon was damaged 3Calorific Pipe was broken |
| Air Cylinder failed to be up& down,ro works slowly | 1 Sealing washer was broken 2 Circuit of electrical magnetic valve was burned 3 The wick of electrical magnetic valve was stuck 4 The wick switch of electrical magnetic calve is not turned on |
| Tolerances exist between indication digits and set-up digits on the temperature control panel | 1 Heating pipe was broken or burned 2 Temperature pipe inspector was broken 3 Temperature table was damaged |
| No Power | 1 Power switch was broken 2 Power circuit was broken |